## Slide 1
NSF FUTURE MANUFACTURING DATA CHALLENGE | FINAL SUBMISSION
Predicting local DED track width from thermal history
Hierarchical condition baselines, local residuals, and nested four-track evaluation
Team Submission
July 31, 2026 | Nested four-track outer validation
Notes: Opening: the model separates condition-level geometry from local variation and evaluates every track as untouched once.
[Sources]
- https://doi.org/10.5281/zenodo.21285367
- https://arxiv.org/abs/2607.07965
- results/improved_submission/metrics.json
- results/improved_submission/outer_fold_predictions.csv
[/Sources]

## Slide 2
THE PROBLEM
Can thermal history predict local geometry after printing?
A DED track is not a uniform line: width and both boundaries vary along x.
Thermal frames record the moving melt pool; profilometry records final geometry.
The modeling task maps a frame and its causal history to the matching local segment.
A credible result must generalize across laser power and quantify uncertainty.
OUR TASK
Predict local width and boundary position from thermal history
Ground truth: center, width, and boundaries from profilometry
Inputs: thermal history; post-process SEM tested separately
Evaluation: four nested leave-one-track-out outer tests
Source: Team analysis of NSF FMRG multimodal DED dataset (Zenodo 10.5281/zenodo.21285367)
2
Notes: Challenge framing: local geometry is a spatial signal; useful predictions must preserve width and boundary variation across power conditions.
[Sources]
- https://doi.org/10.5281/zenodo.21285367
- https://arxiv.org/abs/2607.07965
- results/improved_submission/metrics.json
- results/improved_submission/outer_fold_predictions.csv
[/Sources]

## Slide 3
THE DATA
Three modalities, one physical x-axis, four untouched outer tests
THERMAL VIDEO
400 active frames per track
400 active frames per track at 50 fps.
10 mm/s scan speed gives 0.2 mm per frame.
Size, temperature, gradients, and asymmetry.
Causal history lives in the TIME domain.
SEM IMAGERY
Post-process SEM ablation
Available imagery is post-process.
The processed center band is masked.
Flank texture is tested, not assumed causal.
Selected in zero outer folds.
3D PROFILOMETRY
Local width and boundaries
Robust cross-track substrate detrending.
Connected 30%-height boundary crossings.
0.40 mm physical smoothing window.
Missing acquisition gaps remain excluded.
Every track is untouched once; model, feature family, preprocessing, and calibration are selected only inside the other three tracks.
Source: Team analysis of NSF FMRG multimodal DED dataset (Zenodo 10.5281/zenodo.21285367)
3
Notes: Data: all modalities are registered to physical x; the outer unit is the whole experimental track.
[Sources]
- https://doi.org/10.5281/zenodo.21285367
- https://arxiv.org/abs/2607.07965
- results/improved_submission/metrics.json
- results/improved_submission/outer_fold_predictions.csv
[/Sources]

## Slide 4
OUR APPROACH
From raw frames to leakage-safe nested predictions
1
Extract
Detrend each cross-section and find connected left/right crossings
2
Align
Use physical x in mm; never normalized row position
3
Decompose
Separate condition baseline from local center/log-width residuals
4
Test
Hold out each track once; select candidates inside the other three
Audit rule: geometry, feature choice, model choice, and uncertainty calibration never see the current outer track. Generative AI assisted coding and layout; it did not alter measurements.
Source: Team analysis of NSF FMRG multimodal DED dataset (Zenodo 10.5281/zenodo.21285367)
4
Notes: Pipeline: each outer track is excluded from feature, model, preprocessing, and calibration choices.
[Sources]
- https://doi.org/10.5281/zenodo.21285367
- https://arxiv.org/abs/2607.07965
- results/improved_submission/metrics.json
- results/improved_submission/outer_fold_predictions.csv
[/Sources]

## Slide 5
METHOD — STEPS 1–2
Ground truth first: robust boundaries, then physical alignment
STEP 1 - LOCAL GEOMETRY EXTRACTION
Measure one connected bead in every valid cross-section
Interpolate missing y pixels only within each cross-section.
Fit substrate slope outside the bead shoulders.
Locate connected 30%-of-peak crossings around the central maximum.
Smooth left and right boundaries over 0.40 mm.
STEP 2 - PHYSICAL TIME-SPACE ALIGNMENT
Match each thermal frame to measured x in millimeters
Detect laser shutoff; retain the prior 400 active frames.
Extract hot components above a fixed 1500 K threshold.
Convert time to x at 10 mm/s and 50 fps.
Reject frames more than 0.10 mm from valid profilometry.
Source: Team analysis of NSF FMRG multimodal DED dataset (Zenodo 10.5281/zenodo.21285367)
5
Notes: Geometry: connected profilometry boundaries define positive local width; thermal frames advance 0.2 mm each.
[Sources]
- https://doi.org/10.5281/zenodo.21285367
- https://arxiv.org/abs/2607.07965
- results/improved_submission/metrics.json
- results/improved_submission/outer_fold_predictions.csv
[/Sources]

## Slide 6
METHOD — STEP 3
Separate condition width from local variation
CAUSAL MULTISCALE HISTORY
Describe the pool now, then summarize how it arrived
Pool axes, temperature, mass, gradients, and asymmetry.
Cooling-tail decay, centroid velocity, and shape change.
5-, 10-, and 20-frame slopes, persistence, and changes.
Robust local normalization isolates within-track departures.
CONSTRAINED NESTED MODEL
Predict a track baseline, then local residuals
Track summaries predict baseline center and log-width.
Local history jointly predicts center and log-width residuals.
exp(log-width) keeps width positive; boundaries stay ordered.
Nested folds choose Ridge, elastic net, PLS, spline, or GP.
Source: Team analysis of NSF FMRG multimodal DED dataset (Zenodo 10.5281/zenodo.21285367)
6
Notes: Modeling: causal multiscale history predicts local residuals while track summaries predict condition baselines.
[Sources]
- https://doi.org/10.5281/zenodo.21285367
- https://arxiv.org/abs/2607.07965
- results/improved_submission/metrics.json
- results/improved_submission/outer_fold_predictions.csv
[/Sources]

## Slide 7
RESULTS
Four-track MAE falls 13.1% while boundaries improve
EXHIBIT 1 - FOUR UNTOUCHED OUTER TRACKS
163 µm
Track-balanced MAE
13.1% lower
vs. direct Ridge
Track-balanced width MAE: 0.187 → 0.163 mm.
Worst-track MAE: 0.308 → 0.219 mm.
Mean boundary MAE: 0.180 → 0.148 mm.
Residual correlation: 0.055 → 0.124.
Source: Team analysis of NSF FMRG multimodal DED dataset (Zenodo 10.5281/zenodo.21285367)
7
Notes: Result: four-track width MAE improves 13.1%, worst-track MAE 28.9%, and boundary MAE 17.6%.
[Sources]
- https://doi.org/10.5281/zenodo.21285367
- https://arxiv.org/abs/2607.07965
- results/improved_submission/metrics.json
- results/improved_submission/outer_fold_predictions.csv
[/Sources]

## Slide 8
THE KEY INSIGHT
Local scaling recovers variation and sharpens uncertainty
EXHIBIT 2 - BEFORE / AFTER SCORECARD
WHAT CHANGED
Condition baseline + local residual wins
1. Predicted variation grows from 21% to 36% of measured scale.
2. Conditional intervals cover 91.4% at 0.738 mm mean width.
3. Global intervals cover 94.2% but are wider at 0.824 mm.
4. Width expands from 0.610 mm easy to 0.912 mm hard.
Source: Team analysis of NSF FMRG multimodal DED dataset (Zenodo 10.5281/zenodo.21285367)
8
Notes: Uncertainty: conditional intervals are narrower than global intervals and expand in difficult regions; SEM is not selected.
[Sources]
- https://doi.org/10.5281/zenodo.21285367
- https://arxiv.org/abs/2607.07965
- results/improved_submission/metrics.json
- results/improved_submission/outer_fold_predictions.csv
[/Sources]

## Slide 9
HONEST ASSESSMENT
Improved, but not ready for closed-loop control
Track-balanced R² is -0.34; local predictions still miss structure.
Four tracks cannot establish stability across plates or recipes.
Nested Track 21 MAE is 0.219 mm; the prior 0.139 mm is historical only.
Post-process SEM is selected in zero folds.
No causal substrate claim is supported.
WHAT WOULD CLOSE THE GAP
Add more powers, plates, repeats, and substrate pre-scans.
Register SEM before processing instead of inferring substrate from post-scan tiles.
Calibrate intervals by laser-power regime or hierarchical conformal methods.
Predict a full contour distribution, not only center plus width.
Source: Team analysis of NSF FMRG multimodal DED dataset (Zenodo 10.5281/zenodo.21285367)
9
Notes: Limitations: R2 remains negative, only four tracks are available, and no causal substrate claim is supported.
[Sources]
- https://doi.org/10.5281/zenodo.21285367
- https://arxiv.org/abs/2607.07965
- results/improved_submission/metrics.json
- results/improved_submission/outer_fold_predictions.csv
[/Sources]

## Slide 10
TAKEAWAYS
Separate the condition, then learn the variation
1
Four-track accuracy
Width MAE falls 13.1%; worst-track error falls 28.9%; boundary MAE falls 17.6%.
2
Physical consistency
Positive width and one shared center reconstruct ordered left/right boundaries.
3
Useful uncertainty
Conditional intervals reach 91.4% coverage and expand in difficult regions.
“Condition shifts and local variation are different problems.”
Questions? | github.com/alphons3t/nsf-chuds | github.com/joeyperez1-debug/nsfsubmit
Source: Team analysis of NSF FMRG multimodal DED dataset (Zenodo 10.5281/zenodo.21285367)
10
Notes: Close: separating the condition shift from local variation is the main transferable modeling insight.
[Sources]
- https://doi.org/10.5281/zenodo.21285367
- https://arxiv.org/abs/2607.07965
- results/improved_submission/metrics.json
- results/improved_submission/outer_fold_predictions.csv
[/Sources]